## Slide 1: Power & Thermal (Bring up checklist & overview)
Vinit – IN005850
BSP TEAM

## Slide 2: Agenda
Power checklist
Wake lock Profiler
Thermal Hal service
Horae & Unified intelligent temperature control
ORMS – Introduction
Debug tools & logs
Case studies

## Slide 3: Power
Base Current :
  Standby Current [ Screen OFF <10mA & Screen ON – compare with previous OS]
GPIO Verification
  All GPIO verification [ including camera, MM, wifi etc. ]
  pinctrl-msm.c -> msm_gpio_dbg_show() & /sys/kernel/debug/gpio (http://gerrit.scm.adc.com:8080/#/c/10055522/ )

## Slide 4: wakelock_profiler
Wakelock Profiler
  Need to configure wakelock profiler, so that DCS and power monitor reasons can be identified.
  Flags to enable this feature [defconfig]
    CONFIG_OPLUS_WAKELOCK_PROFILER=y
    CONFIG_OPLUS_POWER_QCOM=y
  Interrupt statics
    \kernel\msm-4.14\drivers\irqchip\irq-gic-v3.c
  alarm statistics
    \kernel\msm-4.14\kernel\time\alarmtimer.c
  Wakeup statistics
    \kernel\msm-4.14\drivers\base\power\wakeup.c
  wakelock_profiler code
    \vendor\oplus\kernel\oppo_wakelock_profiler\

## Slide 5: Statistics of the number of interruptions
Wakeup_reasons_statics is the entry of wakelock_profiler interrupt statistics
WS_CNT_SUM: counts all interrupt times
WS_CNT_MODEM|WS_CNT_WLAN|WS_CNT_ADSP|WS_CNT_CDSP|WS_CNT_SLPI: counts the number of interrupts separately

## Slide 6: Alarm Statistics
alarmtimer_wakeup_count is the entry of wakelock_profiler alarm statistics times

## Slide 7: Wakeup Statistics
Wakeup_reasons_statics is the entrance to wakelock_profiler wakeup statistics

## Slide 8: Wakelock profiler
Initialize wakelock_profiler
  /sys/kernel/wakelock_profiler/ap_resume_reason_stastics
  /sys/kernel/wakelock_profiler/modem_resume_reason_stastics

## Slide 9: Wakelock profiler
interruptions and wakeups:

## Slide 10: Wakelock profiler
Alarm Statistics

## Slide 11: Logs
Kernel

## Slide 12: Other
OPLUS_FEATURE_POWERINFO_RPMH & OPLUS_FEATURE_POWERINFO_STANDBY
Feature and solutions
  Freeze solutions, GPA optimization , multilevel brightness, night network mode etc.

## Slide 13: Thermal
Thermal@2.0 Integration
  thermal-hal_product.mk
  SE Policy related changes
  Thermalconfig.cpp [ changes specific to soc id ]
  DTSI changes

## Slide 14: Thermal : qcom-proprietary changes
platform/vendor/qcom-proprietary/coretech-config-vendor / thermal-hal/thermal-hal_product.mk
device/qcom/sepolicy_vndr / legacy/vendor/common/hal_thermal_default.te
device/qcom/sepolicy_vndr / legacy/vendor/common/file_contexts
  /(vendor|system/vendor)/bin/hw/android.hardware.thermal@2.0-service.qti u:object_r:hal_thermal_default_exec:s0

## Slide 15: Thermal
thermalConfig.cpp
  Add entry in target_therm_cfg map for project soc id along with sensor vector.
  Configure based on soc ID(/sys/devices/soc0/soc_id)

## Slide 16: Thermal Service verification

## Slide 17: Oplus Thermal
  oplus/thermal / dist/prjConfig/horae_source_SDM845.conf

## Slide 18: Unified intelligent Temperature control
my_product/etc/temperature_profile/sys_thermal_control_config.xml
adb shell dumpsys activity service com.coloros.oppoguardelf getThermalConfig
Total of 21 levels are defined ( -1 to 19)

## Slide 19: Unified intelligent Temperature control
CPU is divided into 10 levels & GPU is divided into 5 levels.
Ref: https://doc.myoas.com/pages/viewpage.action?pageId=229896640

## Slide 20: Unified intelligent Temperature control
Application control level capability
  Application control is currently divided into 5 levels. Athena implements different types of cleaning strategies according to the level value transmitted by the intelligent temperature control.
Charge speed limit
  The charging speed limit is divided into 25 levels, and the impact on the charging time and temperature is tested by the thermal design colleagues during the strategic configuration and debugging. Level 0 represents unlimited charging.

## Slide 21: Unified intelligent Temperature control
Camera Control
  camera provides control functions such as turning off the fill light, stopping video recording, adjusting the brightness of the camera scene screen, and turning off the camera.
Brightness Control
  Set multi-level brightness gears, a total of 11 gears, and fix the adjustable range of each gear, such as 100nit/ gear; level 0 means cancelling the temperature control brightness limit.
Likewise there are other parameters which can be controlled..

## Slide 22: Unified intelligent Temperature control

## Slide 23: Unified intelligent Temperature control
tempGear="1" --- represents trigger level 1
cpu="0" --- represents cpu level 0
gpu="0" --- represents gpu level 0
restrict="0" ---Represents application control level 0
brightness="1" --- stands for screen brightness level 1. This function currently has no practical effect.
charge="0" ---represents the charging speed level 0
modem="0" --- represents modem control level 0
disFlashlight="1" --- means turn off the fill light, 1 means turn off
stopCameraVideo="0" ---1 means stop recording, 0 means not stop
cameraBrightness="200" --- represents adjusting the brightness of the camera scene screen, 200 represents the brightness value
disCamera="0" ---1 means to turn off the camera, 0 means not to turn off
disWifiHotSpot="0" ---1 means to turn off the hotspot, 0 means not to turn off
disTorch="0" ---1 means turn off the flashlight, 0 means not turn off
disFrameInsert="0" ---0 means temperature control exits frame insertion and disables control, 1 means frame insertion is disabled
fps="55" --- stands for adjusting the application frame rate, 55 stands for the frame rate value, the default is restored to 120Hz
refreshRate="1" ---1 means to set the refresh rate to 60hz, 0 means to exit the temperature control and take over the screen refresh rate
disVideoSR="1" ---1 means turn off the over-resolution capability, 0 means temperature control exits the over-resolution disable
disHBMHB="1" ---1 closes the HBM highlighting ability, 0 means that the temperature control exits and takes over the HBM highlighting ability
disOSIE="1" ---1 Turn off the ultra-clear visual effect ability, 0 means that the temperature control exits and takes over the ultra-clear visual effect

## Slide 24: ORMS
The system power consumption is reduced as much as possible while ensuring system performance
Mainly it inherit the hypnus philosophy ( scene-based optimization )
  Hypnus module consists of a Linux Kernel (DLKM) and some modifications over Kernel/Android Framework layer.
App launch, scene switch , Sliding
Touch acceleration
Fingerprint , facelock etc.

## Slide 25: ORMS
Scene based customization

## Slide 26: ORMS
What we can control?
  CPU/GPU frequency & other parameters
  Scene based performance enhancement for application or system services
  DDR frequency, Sched, LPM etc

## Slide 27: Debug tools & logs
  Kernel Logs
  Android Logs
  Batterystat and event logs
  Bug report & battery historian
  Systrace
  Power Monitor
  On device debugging
  HW

## Slide 28: Case Studies – Higher Standby 7150R
power decomposition result
  UFS power consumption was more in R
DTSI comparison
  SPM level for UFS was 5, while in Q , spm-level was not set.
FS team feedback
  FS team confirm, that we should remove spm-level from R version also.

## Slide 29: Case Studies - 2706755
16%。 power consumption , Standby 12H
Initial Analysis:
      DIAG_WS wake lock is acquired which has stopped the device to go in deep sleep.
Further Analysis:
      Logkit was running with Modem logs enabled.
Retest after disabling the modem logs , power consumption was normal.

## Slide 30: Case Studies - 2755214
2 hours of screen hold, the test version current is 76.7mA, 59.7mA greater than the standard 17mA
Initial Analysis:
In first set of logs, dexopt optimization was on-going. When QA re-test it , current was still high.
In later set of logs , we found longwake due to com.oppo.ota, after disabling the OTA service current was normal. Later issue transferred to ROM Team for further debugging.

## Slide 31: Case Studies - 2794791
Camera Avg Current was high
Initial Analysis: In systrace, we found the CPU frequency in case of Q is more as compare to P.
Camera Team Analysis: The Recording resolution is upgraded in Q OS , that’s why camera is running on higher frequency.
Test Team : When same issue is tested with same resolution on both P and Q OS, current was same.

## Slide 32: Case Studies - 2790839
The average current of the face recognition test machine is 565.6mA, which is 45.8mA larger than the average current of the contrast machine, 519.8mA
Analysis:
  With the help of systrace we found that in case of Android Q, the frequency is more during face unlock as compare to Android P. When we investigate further with face lock team, we found that algorithm for face unlock is changed, which increase CPU frequency. Due to this the current was higher.

## Slide 33: Thank you!